## Slide 1: DESIGN AND CONSTRUCTION SUN DRYING WET CLOTHES SYSTEM
Hoàng Phi Long – SE62021
Nguyễn Đình Phong - SE61968
Trịnh Bình – SE61780
Team Members:
Mr. Nguyễn Đức Lợi
Supervisor:

## Slide 2: AGENDA
Overview
Implementation
Evaluation
Conclusion
Demonstration

## Slide 3: OVERVIEW
Introduction
Proposed Solution
System Overview

## Slide 4: INTRODUCTION
Current Situation
  Vietnam is a tropical country
  Inefficient clothes drying process during the rainy months
  Available products on market
    Expensive
    Do not have rain detection
    Can only control with RF Remote or manually
    Use general electrical
Notes: Việt nam là một quốc gia nhiệt đới với lượng mưa nhiều. Người Việt nam cũng rất là bận rộn trong cuộc sống hằng ngày nên thường có ít thời gian ở nhà. Vậy nên, nhiều người việt nam thường có thói quen giặt đồ xong phơi vào trời nắng cho mau khô trong lúc đi làm. Về máy sấy, vì máy sấy thường cồng kềnh và tiêu thụ nguồn điện không ít, mà đa phần nhà của người VN khá nhỏ chứ không thật sự rộng rãi nên việc có một máy sấy không được ưa chuộng. Tuy nhiên vào những mùa mưa, khi đi làm xa bất chợt những cơn mưa kéo tới, làm đồ không những ướt mà còn trở nên mau hư hỏng.
Ở trên thị trường cũng có nhiều người làm các sản phẩm giàn phơi tự động, giàn phơi thông minh cos phần tiện lợi tuy nhiên vẫn chưa phù hợp với tùi tiền của người Việt nam cũng như đáp ứng nhu cầu. Bởi vì các dàn phơi hiện nay thường chỉ cung cấp tính năng điều khiển qua remote, sấy đồ, khử khuẩn chứ không giải quyết được vấn đề khi trời mưa. Chưa kể việc giá thành rất là cao. Ngoài ra việc sử dụng năng lượng điện lưới nhà, dẫn tới nếu chẳng may mất điện, thì hệ thống không hoạt động được.

## Slide 5
PROPOSED SOLUTION
Design And Construction Sun Drying Wet Clothes System
Features
  Rain detection
  Automatic controlling
  Using solar energy
  Control via RF Remote, Keypad and Mobile application
  Drying system
Notes: Thế nên, nhóm tụi em mới đưa ra đề tài [X] để khắc phục những cái chưa hay của sản phẩm trên thị trường và đáp ứng được nhu cầu của người dùng ở VN. Bênh cạnh đó nhóm cũng phát triểm thêm công nghệ IoT vào sản phẩm để nhằm nâng cao tính tiện nghi và dễ sử dụng của đề tài.

## Slide 6: SYSTEM OVERVIEW
Energy Block
Sensors Block
Output block
Controller Block
Server and Mobile App block
Input control block

## Slide 7: SYSTEM OVERVIEW

## Slide 8: IMPLEMENTATION
Sensors Details
System architecture
Technology
Performances

## Slide 9: Rain sensor

## Slide 10: Humidity & Temperature DHT11
Temperature:
  0 - 50°C (Error ± 2°C)
Humidity:
  20 - 80%RH (Error: ± 5%)
Maximum sampling frequency: 1Hz

## Slide 11: Light Sensor BH1750
Light Density:
  0 - 65535 lux
Maximum sampling frequency: 1Hz
Notes: Chi tiết đọc: https://github.com/claws/BH1750

## Slide 12: Matrix Keypad (4x4)
Notes: How does it work?
https://www.youtube.com/watch?v=RGkIHFQf8-w
http://pcbheaven.com/wikipages/How_Key_Matrices_Works/

## Slide 13: Limit Switch
Notes: https://www.youtube.com/watch?v=q6nP1FjxAMU

## Slide 14: Limit Switch
Operating voltage: 12VDC
Frequency: 125 rpm
Moment: 20kg.cm
Notes: https://www.youtube.com/watch?v=Zu3TYBs65FM

## Slide 15: Solar Panel
Maximum Power: 10W
Maximum Voltage: 17.07V
Maximum Current: 0.58A
Open Circuit Voltage: 21.21V
Short Circuit Current: 0.63A
Notes: https://www.youtube.com/watch?v=Zu3TYBs65FM

## Slide 16: NodeMCU
Main IC: ESP8266 Wi-Fi SoC
Memory: 128KB
Storage: 4MB
Wi-Fi Standard: IEEE 802.11 b/g/n
Notes: https://www.youtube.com/watch?v=Zu3TYBs65FM

## Slide 17: H-Bridge

## Slide 18: RF Remote PT2272/PT2262
Working frequency: 315MHz
Range in open space: 50-100m

## Slide 19: SYSTEM ARCHITECTURE OVERVIEW

## Slide 20: HARDWARE ARCHITECTURE
IoT Architecture
  Highly scalable and available out of the box due to the nature of each selected component.
  Minimal knowledge required to start.
  It’s scalable and fault tolerant by design.
  Reduces the development and deployment costs and timeframes

## Slide 21: API WEB SERVER ARCHITECTURE
MVC Architecture
  Code is reusable
  Easy to test

## Slide 22: MOBILE APP ARCHITECTURE
Flux Architecture
  Making source code as simple to understand as possible.
  Easier to maintain and reduce time to develop application
  Having supported library (Redux)
  Suitable for React codebase

## Slide 23: TECHNOLOGY
React Native with Expo API
  Easy to learn
  Easy to upgrade
  Cross-platform
  Using Javascript as main language
  Building on cloud

## Slide 24: TECHNOLOGY
MongoDB
  Document Oriented Database
  Easy to use
  Scalable
  Flexible
  Using Javascript for query

## Slide 25: TECHNOLOGY
ExpressJS and NodeJS
  Easy to learn
  Fast and Powerful
  Open source with large community

## Slide 26: PERFORMANCES
Control System from Mobile App Performances
  Request time performance
Network Type | System | Request Time
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | Android Application | 143ms
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | DCDCS System | 252ms
3G | Android Application | 471ms

## Slide 27: PERFORMANCES
Control System from Mobile App Performances
  Response time performance
Network Type | System | Response Time
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | Android Application | 352ms
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | DCDCS System | 461ms
3G | Android Application | 621ms

## Slide 28: PERFORMANCES
Control System from RF Remote/Keypad
Control Type | Distance | Response Time
RF Remote | 0m | 5ms
RF Remote | 50m | 32ms
RF Remote | 100m | 182ms
Keypad | 0m | 5ms

## Slide 29: PERFORMANCES OVERALL
System can detect rain within ~50ms
Server can handle at least 1000 request per second
System works with 95% accuracy
System have multiple options to control

## Slide 30: EVALUATION
Advantages
Disadvantages
Future plans

## Slide 31: ADVANTAGES
Cheap
Rain detection
Have multiple control options
Have dryer system for drying clothes in rainy days
Use solar energy
  Reduce electric bills
  Able to work while electrical blackouts
Easy to extend
System is easy to construct

## Slide 32: DISADVANTAGES
Cannot control via Web application
Rain detection is not able to determine when the rain has stopped
System cannot detect if the clothes is dry or still wet

## Slide 33: FUTURE PLANS
Implement Hidden Markov Models (HMM) for rain forecasting
Build a website for user to check their account information and control the system along with mobile application
Build a system that can detect whenever the clothes is dry or wet.

## Slide 34: CONCLUSION
DCDCS system has a great potential to succeed in the market.
Limitations need to be improved to make the product a competitive advantage over other competitors.

## Slide 35: DEMONSTRATION
Control with RF Remote
Control with Keypad
Automatic control
Control with Mobile Application

## Slide 36: Q&A

## Slide 37: Thank You