## Slide 1: DESIGN AND CONSTRUCTION SUN DRYING WET CLOTHES SYSTEM
Hoàng Phi Long – SE62021 (Leader)
Nguyễn Đình Phong - SE61968
Trịnh Bình – SE61780
Team Members:
Mr. Nguyễn Đức Lợi
Supervisor:

## Slide 2: HEADLINE
Overview
Design
Implementation
Conclusion
Demonstration

## Slide 3: INTRODUCTION
Available products on market
  Expensive
  Do not have rain detection
  Can only control with RF Remote or manually
  Use general electrical
Notes: Ở trên thị trường cũng có nhiều người làm các sản phẩm giàn phơi tự động, giàn phơi thông minh cos phần tiện lợi tuy nhiên vẫn chưa phù hợp với tùi tiền của người Việt nam cũng như đáp ứng nhu cầu. Bởi vì các dàn phơi hiện nay thường chỉ cung cấp tính năng điều khiển qua remote, sấy đồ, khử khuẩn chứ không giải quyết được vấn đề khi trời mưa. Chưa kể việc giá thành rất là cao. Ngoài ra việc sử dụng năng lượng điện lưới nhà, dẫn tới nếu chẳng may mất điện, thì hệ thống không hoạt động được.

## Slide 4: INTRODUCTION
Other research available
  Simple function
  Only have rain detection

## Slide 5: INTRODUCTION
Current Situation
  Vietnam is a tropical country
  Inefficient clothes drying process during the rainy months
Notes: Việt nam là một quốc gia nhiệt đới với lượng mưa nhiều. Người Việt nam cũng rất là bận rộn trong cuộc sống hằng ngày nên thường có ít thời gian ở nhà. Vậy nên, nhiều người việt nam thường có thói quen giặt đồ xong phơi vào trời nắng cho mau khô trong lúc đi làm. Về máy sấy, vì máy sấy thường cồng kềnh và tiêu thụ nguồn điện không ít, mà đa phần nhà của người VN khá nhỏ chứ không thật sự rộng rãi nên việc có một máy sấy không được ưa chuộng. Tuy nhiên vào những mùa mưa, khi đi làm xa bất chợt những cơn mưa kéo tới, làm đồ không những ướt mà còn trở nên mau hư hỏng.

## Slide 6
PROPOSED SOLUTION
Design And Construction Sun Drying Wet Clothes System
Features
  Rain detection
  Automatic clothes collecting
  Dryer system
  System can be controlled to dry/collect clothes, start/stop dryer with
    RF Remote
    Keypad
    Mobile application
  Using solar energy
Notes: Thế nên, nhóm tụi em mới đưa ra đề tài [X] để khắc phục những cái chưa hay của sản phẩm trên thị trường và đáp ứng được nhu cầu của người dùng ở VN. Bênh cạnh đó nhóm cũng phát triểm thêm công nghệ IoT vào sản phẩm để nhằm nâng cao tính tiện nghi và dễ sử dụng của đề tài.

## Slide 7: RAIN SENSORS

## Slide 8: Humidity & Temperature DHT11
Temperature:
  0 - 50°C (Error ± 2°C)
Humidity:
  20 - 80%RH (Error: ± 5%)
Maximum sampling frequency: 1Hz

## Slide 9: Light Sensor BH1750
Light Density:
  0 - 65535 lux
Humidity:
  20 - 80%RH (Error: ± 5%)
Maximum sampling frequency: 1Hz
Notes: Chi tiết đọc: https://github.com/claws/BH1750

## Slide 10: Matrix Keypad (4x4)
Notes: How does it work?
https://www.youtube.com/watch?v=RGkIHFQf8-w
http://pcbheaven.com/wikipages/How_Key_Matrices_Works/

## Slide 11: Limit Switch
Notes: https://www.youtube.com/watch?v=q6nP1FjxAMU

## Slide 12: Limit Switch
Operating voltage: 12VDC
Frequency: 125 rpm
Moment: 20kg.cm
Notes: https://www.youtube.com/watch?v=Zu3TYBs65FM

## Slide 13: Solar Panel
Maximum Power: 10W
Maximum Voltage: 17.07V
Maximum Current: 0.58A
Open Circuit Voltage: 21.21V
Short Circuit Current: 0.63A
Notes: https://www.youtube.com/watch?v=Zu3TYBs65FM

## Slide 14: NodeMCU
Main IC: ESP8266 Wi-Fi SoC
Memory: 128KB
Storage: 4MB
Wi-Fi Standard: IEEE 802.11 b/g/n
Notes: https://www.youtube.com/watch?v=Zu3TYBs65FM

## Slide 15: H-Bridge

## Slide 16: RF Remote PT2272/PT2262
Working frequency: 315MHz
Range in open space: 50-100m

## Slide 17: SYSTEM OVERVIEW
Energy Block
Sensors Block
Output block
Controller Block
Server and Mobile App block
Input control block

## Slide 18: TECHNOLOGY
React Native with Expo API
  Easy to learn
  Easy to upgrade
  Cross-platform
  Using Javascript as main language
  Building on cloud

## Slide 19: TECHNOLOGY
MongoDB
  Document Oriented Database
  Easy to use
  Scalable
  Flexible
  Using Javascript for query

## Slide 20: TECHNOLOGY
ExpressJS and NodeJS
  Easy to learn
  Fast and Powerful
  Open source with large community

## Slide 21: SYSTEM ARCHITECTURE OVERVIEW

## Slide 22: HARDWARE ARCHITECTURE
IoT Architecture
  Highly scalable and available out of the box due to the nature of each selected component.
  Minimal knowledge required to start.
  It’s scalable and fault tolerant by design.
  Reduces the development and deployment costs and timeframes

## Slide 23: API WEB SERVER ARCHITECTURE
MVC Architecture
  Code is reusable
  Easy to test

## Slide 24: MOBILE APP ARCHITECTURE
Flux Architecture
  Making source code as simple to understand as possible.
  Easier to maintain and reduce time to develop application
  Having supported library (Redux)
  Suitable for React codebase

## Slide 25: PERFORMANCES
Control System from Mobile App Performances
  Request time performance
Network Type | System | Request Time
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | Android Application | 143ms
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | DCDCS System | 252ms
3G | Android Application | 471ms

## Slide 26: PERFORMANCES
Control System from Mobile App Performances
  Response time performance
Network Type | System | Response Time
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | Android Application | 352ms
Wi-Fi (Ping 2, Down: 20Mb, Up: 15Mb) | DCDCS System | 461ms
3G | Android Application | 621ms

## Slide 27: PERFORMANCES
Control System from RF Remote/Keypad
Control Type | Distance | Response Time
RF Remote | 0m | 5ms
RF Remote | 50m | 32ms
RF Remote | 100m | 182ms
Keypad | 0m | 5ms

## Slide 28: PERFORMANCES OVERALL
System can detect rain within ~50ms
Server can handle at least 1000 request per second
System works with 95% accuracy

## Slide 29: ADVANTAGES
Cheap
Rain detection
Have multiple control options
Have dryer system for drying clothes in rainy days
Use solar energy
  Reduce electric bills
  Able to work while electrical blackouts
Easy to extend
System is easy to construct

## Slide 30: DISADVANTAGES
Cannot control via Web application
Rain detection is not able to determine when the rain has stopped
System cannot detect if the clothes is dry or still wet

## Slide 31: FUTURE PLANS
Implement Hidden Markov Models (HMM) for rain forecasting
Build a website for user to check their account information and control the system along with mobile application
Build a system that can detect whenever the clothes is dry or wet.

## Slide 32: CONCLUSION
DCDCS system has a great potential to succeed in the market.
Limitations need to be improved to make the product a competitive advantage over other competitors.

## Slide 33: DEMONSTRATION
Control with RF Remote
Control with Keypad
Automatic control
Control with Mobile Application

## Slide 34: Q&A

## Slide 35: Thank You